## Slide 1: Multicore System – GPU Lab 1
Biao Wang | AES

## Slide 2: Outline
Programming GPU using OpenCL
  Platform Components
  OpenCL Code Example
  Thread Configuration
  Compile and execution
Bilinear filter for demosaicing interpolation
  Bayer Patterns
  Obtain G, B at R locations
  Obtain R, B at G locations
  Obtain G, R at B locations

## Slide 3: Programming Model Overview: platform
CPU
In general means GPU, consist of compute units, which in turn consists of processing elements.

## Slide 4: Programming Model Overview: Code Example (I)
//set up OpenCL working environment
clGetPlatform // get platform
clGetDeivceID // get device
clCreateContext // create context
clCreateCommandQueue // command queue
//read kernel source file kernel.cl
...
//build kernel on runtime,i.e online compilation
prog = clCreateProgramWithSource(context,...)
clbuildProgram(prog,...)
//create memory on GPU
clCreateBuffer(..., CL_MEM_READ_ONLY, ...);
clCreateBuffer(..., CL_MEM_READ_ONLY, ...);
//to be continue
//Implement kernel code here
__kernel void bilinearFilter(
__global ushort *input,
__gloabl ushort *output)
{
//define thread mapping, i.e., locate the location of the input data for loading
...
//compute
...
//write results to output
...
}
Host code: OpenCL.cpp
Device code: kernel.cl

## Slide 5: Programming Model Overview: Code Example (II)
//set kernel arguments
clSetKernelArg()... // arg1..
clSetKernelArg()... // arg2..
...
//transfer input data from CPU to GPU
clEnqueueWriteBuffer(...)
//set up thread configuration
gloabl_size[0] = Gx; gloabl_size[1] = Gy;
local_size[0] = x; local_size[1] = y;
//launch kernel
clEnqueueNDRangeKernel(...)
//tranfer output data from GPU to CPU
clEnqueueWriteBuffer(...)
//Implement kernel code here
__kernel void bilinearFilter(
__global ushort *input,
__gloabl ushort *output)
{
//define thread mapping, i.e., locate the location of the input data for loading
...
//compute
...
//write results to output
...
}
Host code: OpenCL.cpp
Device code: kernel.cl
execute

## Slide 6: Thread/workitem Configurations
  Get global work item ID
  get_global_id
  Number of global work items
  get_global_size
  Get local work item ID
  get_local_id
  Number of local work items
  get_local_size
  Get Work group ID
  get_group_id
  Number of work groups
  get_num_groups

## Slide 7: Indexing Example

## Slide 8: Compile & execution
cd demosaicMHC
make
./opencl_demosaic bayered_rainFruits438.png bilinerFilter.cl

## Slide 9: Outline
Programming GPU using OpenCL
  Platform Components
  OpenCL Code Example
  Thread Configuration
  Compile and execution
Bilinear filter for demosaicing interpolation
  Bayer Filter
  Obtain G, B at R locations
  Obtain R, B at G locations
  Obtain G, R at B locations

## Slide 10: Bayer Filter and debayering/demosaicing process

## Slide 11: Bayer Filter and its Patterns
Bayer filter array:
Compared to RGB representation, use one third of samples to save image
G samples take up 50%, R 25%, B 25%
Four patterns:
focus

## Slide 12: Obtain G, B at R locations
B0
B2
G1
R
G3
B3
G2
G0
B1

## Slide 13: Obtain R, B at G locations (I)
B0
R1
R0
G
B1

## Slide 14: Obtain R, B at G locations (II)
B0
R0
B1
G
R1

## Slide 15: Obtain G, R at B locations
R0
G1
B
G0
R2
G3
R3
R1
G2